## Slide 1: Vivisecting Mobility Management in 5G Cellular Networks
Ahmad Hassan†, Arvind Narayanan†, Ruiyang Zhu‡, Anlan Zhang†, Wei Ye†, Shuowei Jin‡, Jason Carpenter†, Z. Morley Mao‡, Feng Qian†, and Zhi-Li Zhang†
†
‡
ACM SIGCOMM’22, Amsterdam, Netherlands.

## Slide 2
source: insiderintelligence.com
What can be done to improve mobility management in future?
What are today’s 5G mobility management practices? Issues?
New mobility management procedures in 5G

## Slide 3: What is mobility management?
4G/5G Core

## Slide 4: Handovers interrupt data activity!
4G/5G Core
Handover is triggered
Data activity gets interrupted

## Slide 5: 5G has made mobility management complex

## Slide 6: 5G has made mobility management complex
Diversity of radio frequency bands
Higher network fluctuations
Small coverage areas
Frequent handovers
Network Heterogeneity
Long handover durations

## Slide 7
Application QoE
Key handover characteristics
Implications on 5G operators
Conduct a comprehensive measurement study of mobility management in 5G cellular networks
3 bandwidth-intensive and latency-sensitive applications
6200+ km, 47000+ handovers
3 large 5G carriers in U.S.
What is the impact of mobility on application QoE?
How frequent are handovers in 5G? How much energy they cost?
What impact does mobility have on the 5G network? Issues?
What can be done to reduce the overhead of mobility?
Handover prediction

## Slide 8: Measurement Testbed
4G/5G Core
Zoom Laptop
Steam cloud play
volumetric server
IPerf server
XCAL Laptop
S21 Ultra phones running 5GTracker
Monsoon power monitor and S20U phone
6,200+ km drive tests in the U.S.

## Slide 9
Impact of mobility on application QoE in 5G

## Slide 10
Live Video Conferencing
4K Cloud Gaming
Volumetric Video Streaming
Impact of handovers on app QoE is still unknown

## Slide 11
1. Radio access technology
2. Handover type
4G radio, 5G radio, 4G  5G
What factors contribute to mobility-induced QoE fluctuations?
3. Network architecture
SA vs. NSA
5. 5G Deployment mode
5G-only vs. dual
4. Radio frequency bands
LowBand, MidBand, mmWave

## Slide 12: Do all handovers have same impact on user QoE?
5G radio
4G radio
2.26x higher latency and 65% higher dropped frame rate for handovers on 4G radio compared to 5G radio
In NSA 5G, handovers on 4G radio are the main culprits for performance loss
Setup:
UE @ Minneapolis
Driving Speed 30 mph
Steam cloud play ; 4K@60FPS

## Slide 13
Key characteristics of 5G handovers

## Slide 14: Energy Overhead of 5G Handovers
130 km/h for 1 hour
3.4 mAh
81.7 mAh
34.7 mAh
Down:4.3GB Up:2GB
Down:75.4GB Up:14.5GB
How does frequent handovers and long handover durations affect the energy consumption of mobile device?
Non-trivial energy footprint for 5G handovers due to high signaling overheads

## Slide 15: What have we discussed so far?
Mobility management in 5G is complex
Application QoE
  5G handovers exert far severe impact on QoE than their 4G counterparts
  The severity is determined by radio technology, frequency band, architecture, and mode
5G handover characteristics
  Interactions b/w 4G and 5G radios significantly increase handover duration in 5G
  Handover energy consumption is non-trivial in 5G due to high signaling overheads

## Slide 16
Implications of 5G handovers on cellular network

## Slide 17: Impact of 5G handovers on network bandwidth
no improvement in median case
5G  5G (inter-gNodeB handover)
Consider the overall handover sequence for 5G  5G handovers
Setup:
UE @ Boston
Driving Speed 30 mph
IPerf Bulk Transfer
14% reduction

## Slide 18: Impact of 4G and 5G radio antenna co-location
non-co-located 4G and 5G antennas
co-located 4G and 5G antennas
consider 4G/5G antenna co-locations during handover decisions
13ms lower latency

## Slide 19
Handover prediction

## Slide 20: What can we do to mitigate the impact of mobility?
Predict handovers
Estimate network fluctuation due to handover
Applications act proactively

## Slide 21
Predict handovers

## Slide 22: System Overview
UE monitors radio environment
UE connects to new cell tower
event triggered and its report sent to cell tower
cell tower makes handover decision
Prognos
Report Predictor
Decision Learner
Handover Predictor
Report Predictor
Decision Learner
Handover Predictor
Model prediction system based on the handover state machine

## Slide 23
Estimate network fluctuation due to handover

## Slide 24: System Overview
UE monitors radio environment
UE connects to new cell tower
event triggered and its report sent to cell tower
cell tower makes handover decision
Prognos
Report Predictor
Decision Learner
Handover Predictor
Report Predictor
Decision Learner
Handover Predictor
Model prediction system based on the handover state machine
handover type +
score

## Slide 25
Applications act proactively

## Slide 26: 16K Panoramic Video Streaming: A Case Study
predicted handover fluctuation (score)  correct ABR throughput estimation
ca
fastMPC
robustMPC
Rate-Based (RB)
Prognos helps improve ABR throughput estimation during handovers
34.6% to 58.6% reduction in stall

## Slide 27: Key Findings and Takeaways
Application QoE
  5G handovers exert far severe impact on QoE than their 4G counterparts
  The severity is determined by radio technology, frequency band, architecture, and mode
5G handover characteristics
  Interactions b/w 4G and 5G radios significantly increase handover duration in 5G
  Handover energy consumption is non-trivial in 5G due to high signaling overheads
Key mobility issues in 5G
  Consider the overall handover sequence for 5G  5G handovers to improve performance
  Consider the 4G/5G antenna co-locations to reduce handover duration
Handover prediction
  Prognos is an on-device solution, and works with any 3GPP-compliant 4G/5G deployment
  It outperforms existing handover prediction methods in our evaluation
  It improves the QoE for 16K panoramic video streaming and volumetric video streaming

## Slide 28
A comprehensive measurement study of mobility management in 5G cellular networks
Arvind
Narayanan
Zhi-Li
Zhang
Ruiyang
Zhu
Shuowei
Jin
Feng
Qian
Z. Morley
Mao
Ahmad
Hassan
Anlan
Zhang
Wei
Ye
Jason
Carpenter
github.com/SIGCOMM22-5GMobility/artifact
1. Application QoE
2. Key handover characteristics
3. Implications on 5G carriers
4. Handover prediction
Our Team
Reach out to us: hassa654@umn.edu